## Slide 1: EDES 301 PCB Project
Mustafa Latif
Due 12/17/2024 @ 11:59pm

## Slide 2: Background Information
We want to have fun lightsaber duels, but prop lightsabers are expensive
  Through this project, we can build our own at a much cheaper cost
  Cost effective, but also cooler since we built them ourselves
  Inspiration/similar projects
    Arduino Lightsaber https://www.instructables.com/Arduino-Based-Lightsaber-With-Light-and-Sound-Effe/
    ENGI 301 Elemental Cosplay Sword https://www.hackster.io/Eunice011/elemental-cosplay-sword-1821f4
Improve upon previous ENGI projects by providing smoother sound effects, motion and impact sensing, and fluid blade ignition

## Slide 3: System Block Diagram
PocketBeagle
(OSD335x-SM SiP)
5V USB battery
GPIO
PWM/
I2S?
I2C
Button
Level Shifter (TXS0108E)
Speaker
(MakerHawk)
Motion Sensor (MPU-6050)
Digital Amplifier (MAX98357)
LED (WS2812B)

## Slide 4: Power Block Diagram
PocketBeagle
(OSD335x-SM SiP)
5V USB battery
GPIO
PWM/
I2S?
I2C
LED (WS2812B)
Speaker
(MakerHawk)
Motion Sensor (MPU-6050)
Digital Amplifier (MAX98357)
3X Buttons
5V
5V
5V
3.3/5V
3.3V
3.9mA
2.75mA
1µA
3.3V

## Slide 5
PocketBeagle off
PocketBeagle in idle state
Lightsaber ignites with ignition sound and light up
Lightsaber in idle state.
No motion: slow light flickering, low humming sounds
motion state:
light flickering, swing sounds
contact state:
light flash white, contact sound
Tap button 2
Cycle through lightsaber colors
Tap button 3
Lightsaber sound mode muted/unmuted
Muted/unmuted current mode feedback sound played
If lightsaber swung
Return to idle
If lightsaber contact
Press button 1
Hold button 2
Hold button 2
Press button 1
Lightsaber de-ignites with de-ignition sound and light off
Return to idle
blade changes color on each press
PocketBeagle power off at any point
Press button 1
Software Block Diagram

## Slide 6: Components / Budget
Component | EDES301 to Buy? | Cost
LED Reel (16.4ft) https://tinyurl.com/4jxemw7m | yes | $27.99
IMU 5pc (1x) https://tinyurl.com/rvzbvbs3 | yes | $12.99
Speakers 2pc (1x) https://tinyurl.com/mrjkcks7 | yes | $11.99
Digital Amplifier 1pc (1x) https://tinyurl.com/ytxx6y4v | yes | $5.95
5V USB battery 2pc (1x) https://tinyurl.com/3b3eus2b | no | $17.99
Note: As some of these parts come with multiple units, Liam and I will be sharing the parts and distributing the costs between us. Thus, the total expenses from EDES301 will not exceed $35 for each of us. Any additional costs will be provided by us.

## Slide 7: Division of Labor
As Liam and I are both working on similar projects, we are dividing systems for each of us to individually work on. The division of labor is as follows:
Mustafa
  Buttons
  LED
  IMU
Liam
  Touch Screen
  Speaker
  IMU
Both of us will work on IMU as this is the main source of data that drives the other components

## Slide 8: Mechanical Drawing
2.9”
3.8”
Pocket Beagle
FRONT
Button
Button
Level Shifter
IMU
Digital Amplifier
LED Strips
Speaker